## Slide 1: Mobile Data Collector Based Data Gathering Technique in a Cluster Based Sensor Network
Submitted by:
Abhilash Majumder
INFORMATION TECHNOLOGY
15/IT/02
Under the guidance of:
Dr.Sanghita Bhattacharjee
DEPARTMENT OF COMPUTER SCIENCE AND ENGINEERING,
NIT DURGAPUR

## Slide 2: Clustering In Wireless Sensor Networks
Mobile sink sensor networks are diversely used to detect and collect information in regions where it is not possible to collect manually. The sensors are divided into clusters of sensors with each cluster containing a fixed number of sensors.
Wireless sensor networks are grouped together into sensor groups called clusters with help of k means algorithm.
Each sensor has an energy given by (Eamp+Eel*l*d*d) where Eamp has a value between 10-100PJ/bits/m^2. The sensors have channel capacity of 1024 KBps.Packet generation rate is 0.02 packet/sec.Length of data packet is 1000bits.
E elec has a value of 50 PJ/bits/m^2. The cumulative value of the total energy per cycle of movement of head/collector is taken into consideration.
Residual energy of the sensors have been calculated to determine the exhausted nodes sensors.
Value of k determines the degree of efficiency of the sensor network and also clustering may produce results which are not optimal. However in long run this algorithm provides optimal solution for large cases and better efficiency than grid based partitioning.
The head /collector collects data from the sensors in a cluster and inquires a latency time from travelling from one node to next intra cluster and also latency between inter cluster transmission.

## Slide 3: Introduction
Wireless sensor network (WSN) refers to a group of spatially dispersed and dedicated sensors for monitoring and recording the physical conditions of the environment and organizing the collected data at a central location. WSNs measure environmental conditions like temperature, sound, pollution levels, humidity, wind, and so on. Sensor nodes sense the area and send sensed data to base station via single or multi hop communication. Due to the small size and low cost of the sensor nodes, they have a very rapid and large application area like military surveillance, environment monitoring, agriculture, health monitoring, etc.
Sensor nodes once deployed in field work unattended. They are highly resource constrained as they have limited processing speed, storage capacity and energy in their on-board battery. All processing done by sensor nodes (sensing, data processing and data communication) is energy consuming. The scarce energy resource and the harsh environmental conditions make replacement or recharging of the battery practically impossible in certain situations like battle field, volcano detection and deep-sea sensing. Thus, energy efficiency of nodes is a key design issue for wireless sensor networks.

## Slide 4: Objective of Clustering Based Approach
Sensor nodes are densely deployed. So multiple sensors are deployed to measure the same or similar physical phenomenon.
Sensor nodes are prone to failure because of battery exhaustion and harsh environmental conditions.
Node failure often changes the topology of a sensor network.
Communication failures are also a critical issue in WSN.
Due to small size, sensor nodes are limited in power, computational capabilities and memory.
The sensors with limited power can also be harnessed using a modified approach of grid based or cluster based system which uses median/centroid analysis
The objective of the clustering is to reduce the overhead of the collector in carrying data from one cluster and to reduce the loss of energy in the other cluster.
It has widespread applications: healthcare monitoring, air pollution monitoring, area monitoring , forest fire detection,landslide detection, natural hazard detection.

## Slide 5: K Means Algorithm for Clustering
Wireless sensor networks have several algorithms for optimisation .One such algorithm is the k means algorithm which induces a partitioning of cluster based on exhaustive iteration.
K means is a machine learning algorithm which uses to partition sensors in to nearest cluster with the help of nearest Euclidean mean distance between the initial k centroids and the sensors.
After addition of sensors into the cluster the average Euclidean distance values and K means is subsequently added again to modify the updated values.
The value of k depends on the user and more partitioning implies dividing the segment into multiple clusters with varying latency times
The optimal partitioning algorithm implies that larger latency sensors should be kept into a fixed partition/ cluster before moving to another cluster. The greater the value of k the less the number of sensors in each cluster. This causes an overhead of travel time by the head but it simplifies the overall energy loss and data is received more.
In case k tends to infinite for large samples the model simplifies as a single sensor grid based model.

## Slide 6: Euler Path in Cluster
The k means algorithm provides a sub-optimal clustering method.However it may be such that the clusters so formed have large intercluster distances which may lead to breakdoqn of the collector head while moving from one cluster to next.
Without optimised motion algorithms for path selection which are NP hard, the collector in sequential search of clusters may result in starvation of some clusters and overdraining of some clusters.
Euler and Hamilton paths are such algorithms based to optimise the path of motion of the collector.
Taking into consideration Euler graph the ,gaph has a Euler path if number of odd degree vertices are 0 and is semieulerian if it has 2 odd degress.
The Euler path /circuit optimised the path as in the fact that it runs a depth first search subroutine and checks for strongly connected components in between the nodes/sensors.
Since the circuit is closed, there exits an optimal solution if all the sensors in a cluster are within a given threshold range .Beyond that range the graph is not feasible and will not have connected component to form a euler/Hamilton /Circular sim[ple tour.

## Slide 7: Methods of Intra cluster Analysis
Intra cluster analysis uses the following calculations:
Packet information rate =X Channel capacity= R and lennth of data packet=L .For X rate the total packet information rate =X*(L/R).
Initial energy of each nodes/sensors are calculated as 5-10 J .
After each sensor provides data to the collector ,it reduces its energy given by total energy- (Eamp +Eel *l*d*d) .This is called residual energy.
Eamp =10-100PJ/bits/m^2 Eel=50nJ/bit.Tha packet generation rate is a constant having an average value of 0.02 packet/sec
The speed of the mobile data collector or head is taken as a constant =20m/s.
Inside the cluster another optimised Euler circuit is created taking in to consideration sensor energy levels and centroid distance and data generation rate.
In the meantime collector services a sensor other sensors gather more information at a rate which changes dynamically.
Intra cluster ltency is the time in seconds which results from moving the head from one sensor to another.

## Slide 8: Methods of Inter cluster Analysis
Inter cluster analysis uses intra cluster analysis as a subroutine.
Each Euler graph which contains distinct clusters are used separately.Inside each cluster intra cluster data collection,and energy calculation, lifetime calculation is done.
In addition to the intra cluster analysis,a new latency time or transmission time is taken into consideration which is the time lag between movement of collector head to another cluster.
The average data generation of two clusters are different as two clusters may have uneven number of sensors given by X*(L/R)*N where N is the number of sensors.
The time taken for the collector to travel from one cluster to another is also used by members of another cluster to gather more information.
Information is gathered as long as the energy of sensors in the cluster does not go below 0 .If majority of the sensors gets exhausted in a cluster the cluster is removed from the multi –graph and the number of graphs in the multi-graph architecture is reduced.
In between the clusters the energy calculations is done and the cycle occurs in circular manner so that each sensor waits for a fixed amount of time initially before it sends its data to the collector.
However if a cluster collapses a new cluster formation k means algorithm is applied to generate new multi-graph architecture.

## Slide 9: Conclusion
In this project, algorithms have been proposed for data gathering using a mobile data collector in a cluster-based wireless sensor network to improve the lifetime and latency. The clusters are generated by k means are further optimized by applying k means when a node sensor dies .This leads to greater output of data and longevity as the edge from the graph containing dead nodes are removed ,which changes overall k means by reducing it. However k means may not always give optimal solution as it is an unsupervised model and in NP hard .Computational algorithms like Travelling Salesman Problem and modified distribution method /assignment method algorithms may offer better solutions than k means. Another algorithm called K nearest neighbors can be also be used. The main topic also lies in identifying if Euler tour always gives sufficient path which is always optimized. Since we are considering sensor nodes in the vicinity of each other and clustering them with k means and creating the graph, there also lies an exclusion of the fact that there may not be a constructive graph to work upon as there may be nodes which are sufficiently further from each other to form a graph.